Specifications of NyARIdMarker version/0.5
(c)2008-2009 nyatla.jp

This document is Specification of Id marker.

# Terms
## Border line
Border line is black area around marker. This area includes a data area.
## Data area
Data area contains some bit data. It is enclosed in border line.
## Dot
Dot is same as a bit of data. This is part of data area.
## Packet
Packet is 1 byte data that is 8 set of Dot.
## Tracking dot
Tracking dot is used for to detect data position. Those are put on around Data dot.
## Control dot
## Data dot
Data dot represents user defined data. This dot can accept any value(0 or 1).
## Domain ID
## Mask ID
## Format ID

# Specification of Border line
Each Border line width is 15% in marker. 70%. The area except border line are data area.

# Specification of Data area.
## Model2
Model2 has a 5*5 data area and 25 dots.

### Structure of bits
Name	Number of bits
Data dot	9[0,1-8]
Tracking bit	10
Control bit1	3
Parity bit	3

Figure 1:index of bit
Figure 2:area of packet
Figure 3:template
### Data dot
Model 2 has 2 packet data that represent at 9 data dots. Packet #0 has one Bit only. It can accept 0 or 1.
Packet #	bit/index of bit / Bit7 Bit6 Bit5 Bit4 Bit3 Bit2 Bit1 Bit0
0	-	-	-	-	-	-	-	0
1	8	7	6	5	4	3	2	1

### Control Dot
Control dot has 2 values.(Mask ID , domain ID)
bit/index of bit
Bit7	Bit6	Bit5	Bit4	Bit3	Bit2	Bit1	Bit0
-	-	-	-	-	12	11	10

Control value is 3bit value except 0x05. The value is given by the following expressions.
control_value=n>=5?n-1:n;

2 values are represented by following definition.
control_value=Control Term(2*3=6 pattern)
Mask ID=control_value%3
Domain ID=control_value/3

### Mask ID
Mask ID specifies mask pattern type of data. Must be set 0.
value	mean
0	No mask
1	Mask type 1 (not support.)
2	Mask type 2(not support.)

### Domain ID
Domain ID specifies data format domain. The domain means the set of encoding and value space, definition.
value	mean
0	RawBit format. (9bit 2packet) This domain means the data is raw format value.
1	-

### Check dot
Check dot value is different according to Domain ID.
Domain ID	mean
0	Check dot means check sum value. / The value is 3bit value except 0x05. The value is given by the following expressions. / n=(packet0+packet1) mod 7. / check_sum=n>=5?n+1:n; / bit/index of bit / Bit Bit2 Bit1 Bit0 / Index of bit 16 15 14 / For example, when data is packet0=1,packet1=120 then check sum=(121 mod 5)=1.
1 or larger	Undefined.

## Model3
Model2 has a 7*7 data area and 49 dots.
### Structure of bits
Name	Number of bits
Data dot	25[0,1-8,9-16,17-24]
Tracking bit	14
Control bit1	5
Parity bit	5

Figure 6:template
Figure 4:index of bit
Figure 5:area of packet
### Data dot
Model 3 has 4 packet data that represent at 25 data dot. Packet #0 has one Bit only. It can accept 0 or 1.
Packet #	Bit/index of bit / Bit7 Bit6 Bit5 Bit4 Bit3 Bit2 Bit1 Bit0
0	-	-	-	-	-	-	-	0
1	8	7	6	5	4	3	2	1
2	16	15	14	13	12	11	10	9
3	24	23	22	21	20	19	18	17

### Control dot
Control dot has 2 value.(mask ID, domain ID)
bit/index of bit
Bit7	Bit6	Bit5	Bit4	Bit3	Bit2	Bit1	Bit0
-	-	-	30	29	28	27	26

Control value is 5bit value except 0x15. The value is given by the following expressions.
control_value=n>=21?n-1:n;

2 values are represented by following definition.
control_value=Control Term(5*3*2=30 pattern)
Mask ID=control_value%5
Domain ID=control_value/5
### Mask ID
Mask ID specifies mask pattern type of data. Must be set 0.
value	mean
0	No mask
1	Mask type 1 (not support)
2	Mask type 2 (not support)
3	Mask type 3 (not support)
4	Mask type 4 (not support)

### Domain ID
Domain ID specifies data format domain. The domain means the set of encoding and value space,
definition.
value	mean
0	RawBit format. (25bit 4packet) This domain means the data is raw format value.
1 or lager	-

### Check dot
Check dot value is different according to Domain ID.
Domain ID	mean
0	Check dot means check sum value. / The value is 5bit value except 0x15. The value is given by the following expressions. / n=(packet0+packet1) mod 31. / check_sum=n>=0x15?n+1:n; / bit/index of bit / Bit Bit4 Bit3 Bit2 Bit1 Bit0 / Index of bit 36 35 34 33 32 / For example, when data is packet0=1,packet1=120,packet2=0,packet3=0, then check sum=(121 mod 31)=28+1=29.
1 or larger	Undefined.

## Model4
データ領域を9*9に分割します。

### 制御ドット
制御語は、２つの値（マスクタイプ、ドメインID）を持ちます。
各値は、以下の式で求めます。
control_value=制御語（5*3*2*2*2=120code）
マスクID=control_value%5
ドメインID=control_value/5
### マスクID
データビットのマスク値を指定します。現在は0のみ指定できます。
値	意味
0	マスクなし
1	マスクパターン1（使用できません）
2	マスクパターン2（使用できません）
3	マスクパターン3（使用できません）
4	マスクパターン4（使用できません）

### ドメインID
データのドメインを表します。
値	意味
0	ユーザ定義空間のRawBit形式データであることを示します。
1	未定義です。

### チェックドット
ドメインIDにより、格納値が異なります。
ドメインID	値
0

## Model5
データ領域を11*11に分割します。
### 制御ドット
制御語は、２つの値（マスクタイプ、ドメインID）を持ちます。
各値は、以下の式で求めます。
control_value=制御語（5*3*2*2*2*2*2=480code）
マスクID=control_value%5
ドメインID=control_value/5
### マスクID
データビットのマスク値を指定します。現在は0のみ指定できます。
値	意味
0	マスクなし
1	マスクパターン1（使用できません）
2	マスクパターン2（使用できません）
3	マスクパターン3（使用できません）
4	マスクパターン4（使用できません）

### ドメインID
データフォーマットのドメインを表します。
値	意味
0	Rawデータであることを示します。
1	-
2以上	互換性のため、使用できません。

### チェックドット
ドメインIDにより、格納値が異なります。
ドメインID	値
0

## Model6
データ領域を13*13に分割します。
### 制御ドット
制御語は、２つの値（マスクタイプ、ドメインID）を持ちます。
各値は、以下の式で求めます。
control_value=制御語（5*3*2*2*2*2*2*2*2=1920code）
マスクID=control_value%5
ドメインID=control_value/5
### マスクID
データビットのマスク値を指定します。現在は0のみ指定できます。
値	意味
0	マスクなし
1	マスクパターン1（使用できません）
2	マスクパターン2（使用できません）
3	マスクパターン3（使用できません）
4	マスクパターン4（使用できません）

### ドメインID
データのドメインを表します。
値	意味
0	ユーザ定義空間のRawBit形式データであることを示します。
1以上	未定義です。

### チェックドット
ドメインIDにより、格納値が異なります。
ドメインID	値
0

## Model7
データ領域を15*15に分割します。
### 制御ドット
制御語は、２つの値（マスクタイプ、ドメインID）を持ちます。
各値は、以下の式で求めます。
control_value=制御語（5*3*2*2*2*2*2*2*2*2*2=7680code）
マスクID=control_value%5
ドメインID=control_value/5
### マスクID
データビットのマスク値を指定します。現在は0のみ指定できます。
値	意味
0	マスクなし
1	マスクパターン1（使用できません）
2	マスクパターン2（使用できません）
3	マスクパターン3（使用できません）
4	マスクパターン4（使用できません）

### ドメインID
データのドメインを表します。
値	意味
0	ユーザ定義空間のRawBit形式データであることを示します。
1以上	未定義です。

### チェックドット
ドメインIDにより、格納値が異なります。
ドメインID	値
0

### Appendix

Parameters of each model.
Name	value
Model	2	3	4	5	6	7
Resolution	5x5	7x7	9x9	11x11	13x13	15x15
Total of bits.	25	49	81	121	169	225
Number of data dot	9	25	49	81	121	169
Number of packets.	1+(1)	3+(1)	6+(1)	10+(1)	15+(1)	21+(1)
Number of control dot.	3(2)	5(4)	7(6)	9(8)	11(10)	13(12)
Control dot value space.	7	31	127	511	2047	4095
Control dot (Number of Mask ID)	3	5	5	5	5	5
Control dot (Number of domain)	2	6	24	96	384	1536
Control dot (Number of bits)	3(2)	5(4)	7(6)	9(8)	11(10)	13(12)

Domain ID
	Model
0	2,3,4,5,6,7	RawBit Format
1	2,3,4,5,6,7	Reserved
2	3,4,5,6,7	Reserved
3	3,4,5,6,7	Reserved
4	3,4,5,6,7	Reserved
5	3,4,5,6,7	Reserved
6	4,5,6,7	Raw-JANCode(13)
7-23	4,5,6,7	Reserved
24-95	5,6,7	Reserved
96-383	6,7	Reserved
384-1535	7	Reserved